## Slide 1: KATHMANDU UNIVERSITY SCHOOL OF ENGINEERING DEPARTMENT OF CIVIL ENGINEERING
Final presentation on
DEMONSTRATIVE MODEL OF ISOLATED AND COMBINED FOOTINGS
Group: 6
Team members
Nilesh Jha (16)
Prabin Kumar Khadka (17)
Suraj Khadka (18)
Sarita Sapkota (44)
Prabin Shah (45)
Saras Mainali (63)
Project Coordinator
Assist. Prof.Vimesh Poudel
Project Supervisor
Er. Sudip Bajgain
Teaching Assistant

## Slide 2: OUTLINES OF PRESENTATION
Introduction
Objectives and limitation
Methodology
AutoCAD Drawing of the project
Model Construction
Work Schedule
Budget
Result and Conclusion
References

## Slide 3: Introduction
Footings
The lowest load bearing structure of the building.
Mainly supports the foundation and the structures, prevents the settling.
Acts as a base to the floor columns and floor walls.
Transfer the vertical loads from columns and floor walls directly to the soil.
Fig: Combined Footing
Source: The Engineering Community;17 July,2021

## Slide 4: Contd…
Types of footing depending on the type of building and the soil bearing capacity.
Shallow foundations (Depth is equal to or less than its width)
  Isolated footing
  Combined footing
  Strap footing
  Mat raft footing
Deep foundations (Depth is greater than it’s width.)
  Deep strap footings
  Pile foundations
  Pier or drill caisson
  Well (cassions) foundation

## Slide 5: Objectives and Limitations
Objectives
Primary Objective
  To prepare the demonstrative model of isolated and combined footings
Secondary Objective
  To understand the application of footings.
  To understand the load transfer mechanism in footing.
  Limitations
  Some of the hooks of stirrups might not be perfectly bent at 135°.
  GI wire was used instead of Fe500TMT rods.

## Slide 6: Methodology
Preliminary study
Literature Review
Calculations
Material Collection
Model Construction
Consultation
Fig: Methodology

## Slide 7: AutoCAD drawing of the project
Fig: Side view of section of Isolated Footing
All dimensions are in mm

## Slide 8: Contd…
Fig: Side view of section of combined footing
All dimensions are in mm

## Slide 9: Contd…
All dimensions are in mm
Fig: Top view of section of combined footing

## Slide 10: Calculation
For Isolated Footing
Name of the Components | Actual Dimension | Reduced Dimension | R.F.
Footing | (150×150) cm2 | 30×30 cm2 | 1:5
Footing depth | 150cm | 30 cm | 1:5
Brick soiling | 230×115×57 mm3 | 50×25×15 mm3 | 1:5
PCC | 7.5cm | 1.5 cm | 1:5
Lower portion volume | (150×150×25) cm3 | 30×30×5 cm3 | 1:5
Height of Truncated Pyramid | 25cm | 5 cm | 1:5
Pedestal | (50×50) cm2 | 10×10 cm2 | 1:5
Column | (30×30) cm2 | 6×6 cm2 | 1:5

## Slide 11: Contd…
For Combined Footing
Name of the Components | Actual Dimension | Reduce Dimension | R.F.
Footing | (300×150) cm2 | 50×25 cm3 | 1:6
Footing depth | 150cm | 25cm | 1:6
Brick soiling | 230×115×57 mm3 | 50×25×15 mm3 | 1:5
PCC | 7.5cm | 1.25 cm | 1:6
Lower portion area | (300×150) cm2 | 50×25 cm2 | 1:6
Height of lower rectangular portion | 150cm | 10 cm | 1:15
Column | (30×30) cm2 | 5×5 cm2 | 1:6
Distance between the center of columns | 150cm | 25cm | 1:6

## Slide 12: Contd…
For Isolated Footing
For Combined Footing
Ingredients | Quantity
Cement | 5.05kg
Fine Aggregate | 5.6kg
Coarse Aggregate | 12.6kg
Water | 2.8L
Ingredients | Quantity
Cement | 7.16kg
Fine Aggregate | 7.96kg
Coarse Aggregate | 17.85kg
Water | 3.93L

## Slide 13: Model Construction
Formwork Preparation, brick laying and PPC for isolated footing

## Slide 14: Contd…
Column and base reinforcement of isolated footing

## Slide 15: Contd…
Isolated footing

## Slide 16: Contd…
PCC and the reinforcement of combined footing

## Slide 17: Contd…
Combined footing

## Slide 18: Work schedule
Work | Week |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
Consultation and Literature Review |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Calculation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Proposal Defense |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Material Collection |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Model Construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mid-term Presentation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Finishing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Final Report Submission and Presentation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Work Completed | 
INDEX

## Slide 19: Budget
S.N. | Materials | Quantity (kg) | Rate (Nrs) | Total Cost (Nrs) | Remarks
1. | GI-Wire | 3 | 230.00 | 690.00 | 
2. | Binding Wire | 1 | 200.00 | 200.00 | 
3. | Cement | 12.21 | 60.00 | - | Provided by Construction lab
4. | Fine Aggregate | 13.56 | 3710 per m3 | - | 
5. | Coarse Aggregate | 30.45 | 3750 per m3 | - | 
Grand Total |  |  |  | 890.00 | 

## Slide 20: Result and Conclusions
Demonstrative model of isolated and combined footing is constructed.
Application of footings in a building structure were known.
Load transfer mechanism in footing is known.

## Slide 21: References
(n.d.). Retrieved from gharpedia.com: https://gharpedia.com/blog/various-types-of-footings-for-your-house/
civiltoday. (n.d.). Retrieved from Civil Engineering: https://civiltoday.com/geotechnical-engineering/foundation-engineering/161-types-of-foundation
Lamichhane, M. B. (n.d.). National Reconstruction Authority. Retrieved from http://www.nra.gov.np/en/news/details/u3uOGsBqXMUqgPk18I08ST5CKg6sGoXcMasExfjc3ao
IS456.2000.pdf

## Slide 22
Thank you !